## Slide 1: MAREA 2. Design and Optimization of a Distributed Communications Middleware
Santi Pérez Fernández
Director: Juan López Rubio
November 2013

## Slide 2: Index
Objectives
System architecture
  Network system architecture
  Service container
Tools & Libraries
Performance results
Conclusions
Future work

## Slide 3: Objectives
Performance optimization
  Network system architecture
New features
  Service implementation based on deployment unit concept
  Naming service

## Slide 4: System Architecture

## Slide 5: Network System Architecture: Router
Creates and manages network lanes
  Lane: A set of references to the bindings establish between the different network architecture elements (encoder and transports) used at a particular moment
  Lane implementation: linked lists of delegates or multicast delegates
Router & network lanes build a highly reconfigurable and adaptive architecture

## Slide 6: Network System Architecture: Transports
Provides communication facilities to send and receive data (byte sequences) from the network (TCP & UDP protocols)
One thread for each individual transport
  Drawbacks: Poor management of large number of threads, memory overhead (1 MB/thread native and CLR)
  Improvement: TCP and UDP asynchronous transports based on asynchronous I/O operations (without threads)

## Slide 7: Network System Architecture: NetworkMessage Pool
Problem: Garbage collection executed by .NET virtual machine can introduce non deterministic pauses
Solution: Use a memory pooling mechanism. Reduce the amount of work that has to be done by the garbage collector and consequently minimize the time used by its own execution
Implementation: NetworkMessage pool based on FIFO queue discipline
Echo test (requester side)
1000 Bytes, 10000 times, 100 Hz

## Slide 8: Network System Architecture: Coder layer
Several encoding layer implementations
Drawbacks:
  XMLSerializer, BinaryFormatter: Overhead
  MAREA Coder (v.1): Custom serialization drawbacks: complexity and maintenance
  Improvements:
  MAREAGen tool: Automatic serialization/deserialization code generation for classes marked as serializable
  Long switch statements are avoided

## Slide 9: Network System Architecture: Coder layer
MAREAGen
  Eliminates the need for MAREA programmers to implement specific serializing and deserializing code
  Creates proxies automatically
  Reduces the size of the serialized data
MAREA
Test
Service
MAREA Gen
MGenTypes.dll
*.cs files
    MAREA 1
    48 B
    118.28 µs
    MAREA 2
    18 B
    0.71 µs

## Slide 10: Network System Architecture: Coder layer
Limitation removal:
  Compatibility with UTF8 character encoding
  Overflow exceptions for high values (double.MaxValue) in double types
  Support for run-time/dynamic Enum types
  Full support of polymorphic capabilities: Inheritance and control of null objects in object trees
New features:
  Support for some of the most commonly used .NET collection types (e.g. lists, dictionaries and hash tables)

## Slide 11: Network System Architecture
Output lane
Serialize (NetworkMessage)
Send (NetworkMessage)
Input lane
Deserialize (NetworkMessage)
Receive (NetworkMessage)
Protocol Message

## Slide 12: Naming service
The naming service allows MAREA to find, share and access services and its communication primitives hiding the network complexity.
Service identifier-> four different hierarchical levels
/<subsystem>/<node>/<instance>/<service>/<primitive>
  Types
    Single addressing: represent a unique primitive or service
    e.g. /Vehicle 1/Devices/Main/GPS
    Query addressing: represent a group of primitive or services inside the network or MAREA domain
    e.g. */Vehicle 1/Devices/*/GPS

## Slide 13: Service Container: Deployment Unit Concept
Deployment Unit: compressed file that contains a module of code loadable by the service container
  Interface Deployment Units (IDU): Contains the interface and description of the service
  Service Deployment Units (SDU): Contains the implementation of the service. It has a dependency with its corresponding IDU
  Library Deployment Units (LDU): Contains libraries or other dependencies required by the service
Benefits
  Types and parameters of service description and implementation are checked at compile time
  Provides flexibility to change parts of a module/sub-system at anytime
  Freedom to change implementations and not break them
RadoelectricAlt: IAltimeter
BarometricAlt : IAltimeter
IAltimeter
Service Implementations
Service Description

## Slide 14: Service Container
MAREA 2 offers an pluggable protocol layer.
  New protocols can be added and removed easily
  Service management and discovery is independent of protocol implementation

## Slide 15: Service Container: Proxies
Are objects that could represent a remote service or set of services selected by a query.
Characteristics:
  Same interface as the represented service
  Act as redirectors. Not extra specific functionality
Types:
    Remote producer proxy: implement transparent communications
    Query proxy: used to support the naming service

## Slide 16: Service Container: Service Manager

## Slide 17: Service Container: Remote & Proxy services

## Slide 18: Protocol Layer
  Service discover of remote services and specific remote message management for each communication primitive
Protocols
  Discovery: Advertise and discover services
  Publish-Subscribe: Subscription and data transfer of variable and event primitives
  RPC: Point to point synchronous communication to implement remote invocation primitive

## Slide 19: Protocol Layer
  Enhancements
    The new design decouples the different protocols into smaller independent modules
  Easily allow to plug additional protocols for implementing other primitives and other communication features
    Discovery protocol is accomplished at service level
      Less network traffic (low throughput networks)
  Support of session tokens as a way to avoid reply attacks in remote invocation primitive

## Slide 20: Tools & Libraries
Thorn

## Slide 21: Tools & Libraries
Unit testing and Continuous integration allows the automated test of functionalities without user intervention. 365 tests assure MAREA 2 correct behavior

## Slide 22: Performance Results: Memory Allocation
Bytes Allocated | MAREA 1 | MAREA Backport | MAREA 2
Variable | 15834797234 | 85587107 | 139311411
Event | 14805029654 | 54609735 | 122285449
MAREA 2 Memory Allocation Reduction:
Variables -> 99.12%
Events -> 99.17%

## Slide 23: Performance Results: RTT
RTT [ms] | MAREA 1 | MAREA 1 Backport | MAREA 2
Variable | 0.8312 | 0.2797 | 0.3622
Event | 0.9421 | 0.3921 | 0.4633
STD-RTT [ms] | MAREA 1 | MAREA 1 Backport | MAREA 2
Variable | 0.6594 | 0.2992 | 0.4081
Event | 0.5453 | 0.5221 | 0.5737
MAREA 2 RTT Reduction:
Variables -> 56.42%
Events -> 50.82%

## Slide 24: Future Work
Addition of new protocols: file-based data transfer protocol, P2P
Static name resolution support
Extend capabilities to other platforms: .NET Compact framework, .NET Microframework, Mono & IOSharp (Raspberry)
Performance optimization: Service container, new implementation in C++, Alternative
QoS control mechanisms: adaptive message QoS control in the service container
Software usability: Specific Visual Studio project templates (IDU & SDU), service distribution (NuGet)

## Slide 25: Conclusions
  A new version of the middleware MAREA 1, has been designed and implemented
MAREA 2 presents a more modular, flexible and reusable architecture. Starting point for providing reflective and adaptive capabilities
The new service implementation based on the deployment unit concept takes benefit from interfaces and the Composite Reuse Principle
Support of a naming service based on dynamic name resolution. Provides fault tolerance to the system
Performance optimization work is focused in the components of the network layer (MAREAGen/MAREA Coder, memory pool mechanism, TCP and UDP asynchronous transports)

## Slide 27: Performance Optimization Results
Echo test
Middlewares: MAREA 1, MAREA 1 network backport, MAREA 2
Test configuration: 100 Hz, 1000 Bytes, 10k times
Key performance parameters: RTT, memory allocation

## Slide 28: Network System Architecture: Coder layer
127 | -
Keys | Values
0 | *FromPublish
1 | *FromDiscover
65 | *FromInt32
66 | *FromUInt32
64 | -
128 | *FromTransportAddress
129 | *FromPosition
Compatible Signatures
Serialization
(object o, byte[] buffer, ref int offset)
Deserialization
(byte[] buffer, ref int offset)
Null
Basic types
Not null
Other
Serialization: Hastable of delegates
Deserialization: Array of delegates
Message Ids from MAREA protocol messages are reused in the service container to proccess the incoming messages
MAREA protocol messages